## Slide 1: Waves
Introduction
Definition
Classification
Wave parameters
Standing Waves
Wave theories
Beaufort scale
Spilling and breaking waves
Tsunamis
Seiches
Internal waves

## Slide 2
Alternative rise and fall of a portion of water surface
wind
  Produced by Movement of objects in to or within the water
  Vibrations(earthquake of basin)
  Transfer of energy into the water from wave inducing sources take place

## Slide 3
Two basic type of waves
Progressive waves
Standing wave (seiches)
Mores forward across water from the area it was formed
Remain where they are produced and appear as a rocking back and forth of the water surface

## Slide 5
Size and type of wind-generated waves are controlled by: wind velocity, wing duration, fetch, and original state of sea surface.
As wind velocity increases wave length, period
and height increase, but only if wind duration
and fetch are sufficient.
Fully developed sea is when the waves
generated by the wind are as large as they
can be under current conditions of wind
velocity and fetch.
Significant wave height is the average wave
height of the highest 1/3 of the waves
present and is a good indicator of potential
for wave damage.

## Slide 6
Catastrophic waves
  Are sudden violent and temporary waves
  Caused by earthquakes, volcanic activity, landsholes in ocean
  Types of catastrophic waves are tsunamis, landslide surges and storm surges
Shallow water wave- Waves in water shallower the ½
Shear wave- oceans that vibrate particulars-back & forth at right angles to direction of wave propagation

## Slide 7
Surface waves
Internal waves

## Slide 8: Difference between surface and long waves
Surface wave | Internal wave
Wind driven Also called capillary waves | Occur on boundaries between water masses of different density with in ocean
Rough, fast and unstable | Internal waves are smoother slower, more stable and attain greater wave height
Surface wave can be up to 20m height | Internal waves can reach a height of about 300m or more
Surface waves require more chargy for generation | Internal waves require less energy for generation

## Slide 9: Characteristics of waves
Include crust at the top trough at bottom
Difference in elevation between crusts and trough is the wave height
Distance between crust or trough-wave length water steepness– The ratio of wave height to wave length
Capillarity is the initial restoring for any body of water
As wind blows – they create pressure and stress– and created capillary waves.
Capillary waves- 1.74cm wave length
As wind increased-Capillay wave developments increase-sea become rough
The capillarity force-become gravity wave and curve length increases-progressive wave

## Slide 10
Ocean and lakes are orbital progressive wave
The wave form moves forward with a steady velocity, so it is called “progressive”.
Wave period is the length of time it takes for a wave to pass a fixed point steepness is defined as the ratio of the wave
Waves with constant wavelength Waves touch bottom
When the wave builds and reaches a steepness greater than a ratio of 1:7, the wave breakes and spills forward.
Breakers are normally assoicated with shorelines, where they are known as surf

## Slide 11
Waves in water deeper than half their wavelengths are known as deep water waves.
Their speed in meters per second can be approximated by the equation speed =g T/2∏, where T is the wave period and g is the acceleration due to gravity (9.8 meters per second squared).
Shallow water waves are those movign in water less than one-twentieth the depth of their wavelength.
Shallow water waves include both seismic sea waves (tsunamis) generated by earthquakes at sea, and tide waves generated by the attraction of the Moon and the Sun on the ocean.

## Slide 12: Standing waves
Also called stationary waves or seiches
Appears as a rocking back and forth of the water surface or an internal boundary with in water column
The line at which the seiche rocks is called node and it experiences no vertical motion.
Antinode is point where vertical motion is maximum
Simple seiche: Has one node in centre and two antinodes at opposite edges.
Complex seiche: May have more nodes and antinodes.
Period of seiche: The time required for the water surface to rock back and forth once and is dependent upon the length and depth of the basin.

## Slide 13
Seiche period (Closed basin) T = 2l gd
Open ended basin T = 4 l
L= length of basin
D=water depth
G=gso cm/tec 2
Standing waves are trigerred by tectonic movements
Seiches display interference, refraction and reflection but they do not move water in circular to elliptical orbit
gd

## Slide 14: Wind produced waves
Wind generated waves are sea,swell, and surf most waves are produced by storm systems
Sea- wind transfers-energy-to water-wave
building under storm system-in area of
mixed wave type called sea.
-fully developed sea is the maximum single the wave can grow under conditions of wind speed, duration and feteh.

## Slide 15
Swell B:As winds move away form they ruffle them they attain uniform pattern and move in trains of equivalent period and height called swells
Surf: As swell B reach shore they are shortened and the crest increases more swiftly which are called surf
It does not have circular motion of wave particles as that of sea and swell.

## Slide 16: Wave parameters
Include - wave length
-wave height
-amplititude
-wave period and wave frequency
Wave crust – highest point of wave
Wave trough-lowest point of wave
Wave length (L)=length from one wave crust to adjacent wave crust or trough
Wave height(H) vertical distance from wave crust to wave trough
Wave amplitude(A) vertical distance of the crest or trough from the flat undisturbed water level (A=1/2 H)
Wave period: amount of time required for one wave length to pass a fixed point.
Frequency(F) is the number of waves passing a fixed point in a unit time.
Celerity(C) is the velocity with which a wave form travels.
Wave stability or steepness is the ratio of wave height to wave length.

## Slide 18: Waves Theories

## Slide 21: Beaufort Scale
Sea State | Beaufort Number | Terminology | Wind Speed (miles per hour) | Average Wave Height (feet) | Description
0 | 0 | Calm | 0-1 | 0 | Sea like a mirror
1 | 1 | Light air | 1-3 | 0.005 | Ripples with appearance of scales; no crests
2 | 2 | Light breeze | 4-7 | 0.18 | Small wavelets; crests have glossy appearance but do not break.
3 | 3 | Gentle breeze | 8-12 | 0.19-1 | Large wavelets, crests begin to break; foam of glossy appearance; a few white horses.

## Slide 22
 | 4 | Moderate breeze | 13-18 | 2-3 | Small waves becoming longer form; many white horses formed; some spray
4 | 5 | Fresh breeze | 19-24 | 4-5 | Moderate waves taking longer form; many white horses formed; some spray
 | 6 | Strong breeze | 25-31 | 6-10 | Large waves begin to form; many white crests more spray
 | 7 | Moderate gale | 32-38 | 11-16 | Sea heaps up; white foam from breaking waves begins to be blown in streaks
5 | 8 | Fresh gale | 39-46 | 17-28 | Moderately high waves of greater length; edges of crests begin to break into spindrift; foam blown in well marked streaks spray affects visibility.

## Slide 23
 | 9 | Strong gale (storm) | 47-54 | 29-40 | High waves; dense streaks of foam along wind direction; sea begins to roll; visibility affected
 | 10 | Whole gale (heavy storm) | 55-63 | 41-59 | Very high waves with long overhanging crests; sea takes white appearance; rolling heavy; visibility affected.
 | 11 | Violent storm | 64-72 | 60-73 | Exceptionally high waves; small and medium sized ships lost from view; crests blown into froth.
 | 12 | Hurricane | 73-82 | 74-80 | Air filled with foam and spray; sea completely white with driving spray; visibility very seriously affected.

## Slide 24: Spilling and breaking waves
Types of breakers
Breaking waves also called breakers
  Found in all beaches
  a

## Slide 25
Types of breakers
Spilling Plunging Collapsing Surging
Unstable top spills over front of waves
Wave curst curls forming air pocket
Large splash of water and foam is thrown in to air
Gentle sloping area
Break in middle of wave
Slides up and down the beach form in steep sloping bottom area

## Slide 26: Tsunami
Trigged by earthquake, volcanoes or land sludes melting of icebergs and sudden movement of earth crust.
These are seismic sea waves
Most common in pacific ocean and not in atlantic and indian ocean
Caused by displacement of earth crust below sea.
Displacement causes sudden rise or fall in the sea surface level above it

## Slide 27
Rise of earth crust below ocean-causes suddenly elevated water to return to equilibrium surface level.
Depression of crust at ocean bottom-gravity forces cause surrounding water to flow in to it.
Both result in production of wave with long wave length (100 to 200km)
These seismic waves radiate from the point of seismic disturtabance at gD
Tsunami have its height of 1 to 2m distributed over its many km wave length

## Slide 28
The energy of tsunami-distributes from ocean surface to oceanfloor and overlength of wave
When the patho fisheries college and research centre wave is bleeked by coast or island the wave energy is compressed in to a smaller water volume as the depth rapidly decreases.
This rapid and sudden increase in energy density causes the wave height to build rapidly and loss of energy is also rapid when wave breakes.
Tremendous surge of moving water races up over the land destroying building docks and trees

## Slide 29
Tsunami effects an area earth radius more than 150km
Can have wavelength up to 1000 km
It comes in waves after waves and the third to 8th waves are most dangerous as they are largest.
The leading edge of tsunami wave group may be either a crust or a trough.
If the curstal disturbance was an upward motion a crust is formed, if the crustal motion was down ward a trough is formed.
It trough arrins first –sea level drops expose seaplants and animals

## Slide 30
Prediction – different can be detected only if it reaches the coast
Even if it effects one coast due cannot predict weather it hits other coast
As the wave more fast (700km/hr across deep water) it is not possible to evaluate the population immediately.